## Slide 1
PETROCHOICE · AI ENGINEER CANDIDATE · ROUND 2
Forklift and Pallet Detection
YOLO11s fine-tuned from COCO, with a live FastAPI demo
Rana Nasser

## Slide 2
AGENDA
What this presentation covers
Then: Done, limitations and next steps .
Approach
1
Problem framing and model choice
Implementation
2
Data pipeline, training and evaluation setup
Key technical decisions
3
What was chosen, why, and the evidence
Final outcome
4
Results, errors, deployment and live demo
Forklift and Pallet Detection ·

## Slide 3
APPROACH
What a forklift and pallet detector enables
Task: object detection on warehouse images. Output: a box, a class and a confidence for every object. Classes: forklift and pallet, empty or loaded. Boxes are enough for counting and zones, and far cheaper to label than masks.
Safety
Warnwhen a forklift enters a walking zone
Automation
Guide autonomous forklifts to the right pallet
Inventory
Count pallets without manual stock checks
Efficiency
Measureforklift use and dock activity
Forklift and Pallet Detection ·

## Slide 4
What is in the image? One label for the whole image, no position.
What is where? A box, a class and a confidence for each object.
Which pixels belong to each object? Slower, and labels cost far more.
TASK TYPE
Our problem is detection: what is where
Classification
Detection
Segmentation
Forklift and Pallet Detection ·
Our task

## Slide 5
Warehouse images and video frames
•Small, distant and partly hidden pallets
•Look-alikes: pallet trucks, stillages, small load carriers •Public data that may not match the target warehouse
A box, a class and a confidence for every object
forklift and pallet, empty or loaded
THE TASK
Detect forklifts and pallets in warehouses
Input
Output
Classes
Why it is hard
Forklift and Pallet Detection ·

## Slide 6
Tools: Python, Ultralytics YOLO, PyTorch, Kaggle Notebooks, with transfer learning from COCO weights. YOLO11n is the lightweight baseline and YOLO11s is compared against it. The choice is revisited on accuracy, speed and hardware.
APPROACH
A single-stage YOLO11 detector, fine-tuned from COCO
Option
Two-stage (Faster R-CNN) Transformer (RT-DETR) YOLO11 (chosen)
Strength
Strong accuracy, good on small objects No NMS step, strong accuracy
Real-time, mature tooling, COCO weights, simple ONNX export
Trade-off
Slower and heavier to deploy
Heavier, needs more data and compute Less accurate on tiny objects than larger models
Forklift and Pallet Detection ·

## Slide 7
IMPLEMENTATION
From raw datasets to a working service
Audit and filter
1
Merge two datasets, keep two classes, validate every label
Split
2
Train, validation and test with a near- duplicate check
Train
3
YOLO11n and YOLO11s from COCO weights at 768 px
Evaluate
4
Select on validation, test once, per-class and error analysis
Deploy
5
ONNX export and a FastAPI demo with saved reports
Forklift and Pallet Detection ·

## Slide 8
IMPLEMENTATION: DATA
Two public datasets, filtered to two classes
Warehouse (Roboflow Universe)
1,075 images, 5classes.11,776palletboxes but only 5 forklift boxes in train.
Forklift (Kaggle)
1,011 images,classesforklift and person. 1,000 forklift boxes in train, no pallets.
1,660
213
187
Forklift and Pallet Detection ·
Rules: exact class-name match (pallet_truck is never pallet), removed classes become background, 80 hard-negative images kept, 3 untrusted images dropped, polygons converted to boxes. Near-duplicate check: 0 images removed.
train images
validation images
test images

## Slide 9
IMPLEMENTATION: DATA
Three data problems and how each is handled
Labels missing across sources
0
pallet boxes in the forklift dataset, and only 5 forklift boxes in the warehouse one. Handled: errors reported per source. Pseudo-labelling exists but is off in the final run.
Class imbalance
12 : 1
palletboxes per forklift box (13,275 against1,101). Fix: forklift images repeated up to 3 times and class- weighted loss (power 0.5). AP is reported per class.
Small objects
70.4%
ofallboxes cover under 1% of the image. Fix: 768px input keeps small pallets visible,and recall is reported by object size.
Forklift and Pallet Detection ·

## Slide 10
YOLO11n and YOLO11s, COCO-pretrained, fine-tuned on the merged data
Mosaic off for the last 10 epochs. No vertical flip, because an upside-down forklift is unrealistic
768 px images, up to 80 epochs, early stopping, cosine learning rate, fixed seed
Model and confidence threshold are chosen on validation. The test set is used once.
TRAINING
Same data, two model sizes, one honest selection
Models
Augmentation
Settings
Selection
Forklift and Pallet Detection ·

## Slide 11
Image resized to 768 px Keeps small pallets visible
COCO weights already know vehicles
Convolution blocks and attention extract features
Mixes features from three scales
Small pallets and big forklifts in one model
Why YOLO11: real-time speed, simple ONNX export, and COCO pretraining lets fine-tuning work with about 2,000 images.
Anchor-free box and class branches, then NMS
No anchor tuning, one pass
ARCHITECTURE
YOLO11: one pass from image to boxes
Input
Backbone
Neck
Head
Forklift and Pallet Detection ·

## Slide 12
ARCHITECTURE
YOLO11: one pass from image to boxes
Forklift and Pallet Detection ·

## Slide 13
KEY TECHNICAL DECISIONS
What was chosen, why, and the evidence
Decision
YOLO11, single-stage
768 px input
Forklift and Pallet Detection ·
Repeat forklifts x3, class-weighted loss
Select on validation, test once
NMS IoU 0.7, confidence 0.35
ONNX for serving
About 12 pallet boxes per forklift box
No tuning to the test set
Best mAP50-95 and best F1 on validation
Faster, no PyTorch needed
Why
Real-time, COCO weights, simple ONNX export
70% of boxes cover under 1% of the image
Evidence
210 ms per image on CPU with ONNX
Small pallets are still the weakest case (62.5% found)
Forklift AP50 0.902, no class mix-ups
YOLO11s 0.491 against 0.476 val mAP50-95
0.491 at IoU 0.7, 0.476 at 0.5
210 ms against 254 ms, mAP50-95 0.532 against 0.540

## Slide 14
Model YOLO11n YOLO11n YOLO11s YOLO11s
Split val test val test
FINAL OUTCOME: RESULTS
YOLO11s is selected on validation; both reach mAP50 above 0.83
mAP50 0.830 0.875 0.838 0.863
mAP50-95 0.476 0.548 0.491 0.540
Precision 0.855 0.869 0.867 0.826
Recall 0.773 0.806 0.778 0.793
YOLO11s has the higher validation mAP50-95 (0.491 against 0.476), so it is selected. On test the two sizes are close. Test-time augmentation raised validation mAP50-95 to 0.507 but more than doubled inference time, so it is not used.
Forklift and Pallet Detection ·

## Slide 15
RESULTS
Both sizes reach mAP50 above 0.85 on the test set
Model YOLO11n YOLO11n YOLO11s YOLO11s
Split val test val test
mAP50 0.830 0.875 0.838 0.863
mAP50-95 0.476 0.548 0.491 0.540
Precision 0.855 0.869 0.867 0.826
Recall 0.773 0.806 0.778 0.809
Forklift and Pallet Detection · first run, 640 px, before class balancing
YOLO11s has the higher validation mAP50-95 (0.491 against 0.476), so it is selected. On test the two sizes are close.
Test-time augmentation raised validation mAP50-95 to 0.507 but more than doubled inference time, so it is not used.

## Slide 16
FINAL OUTCOME
Forklift AP50 0.902, mAP50-95 0.631. Pallet AP50 0.823, mAP50-95 0.450
Trained model and ONNX export, FastAPI live demo with saved reports, GitHub repository, README and
technical documentation
YOLO11s on the held-out test set
0.863
mAP@0.5
0.540
mAP@0.5:0.95
0.826
Precision
0.793
Recall
Per class
Delivered
Forklift and Pallet Detection · 11

## Slide 17
FINAL OUTCOME: ERRORS
Precision 0.775, recall 0.774, F1 0.775 at the validation-chosen threshold
Pallets found by size: small 62.5%, medium 83.3%, large 86.9%
Missed objects are small: median area 0.19% of the image against 0.42% for all boxes
Where the model still fails at confidence 0.35
943
correct detections
273
false alarms
275
missed objects
0
forklift / pallet mix-ups
Forklift and Pallet Detection · 12

## Slide 18
FINAL OUTCOME: DEPLOYMENT
ONNX export keeps accuracy and runs without PyTorch
210 ms
per image on CPU with ONNX
(4.8 FPS)
254 ms
per image on CPU with PyTorch
(3.9 FPS)
0.53
ONNX test mAP50-95, against 0.540
in PyTorch
Measured on a Kaggle CPU (Intel Xeon 2.0 GHz), batch 1, 768 px. On the Tesla T4 inference takes about 13 ms. Speed on other hardware
differs: a laptop CPU in the demo needs roughly half a second per image. YOLO11s has 9.4 M parameters and 21.4 GFLOPs.
Forklift and Pallet Detection · 13

## Slide 19
FINAL OUTCOME: LIVE DEMO
A FastAPI service with a browser UI
1. Upload
One or many images, drag
and drop
2. FastAPI /predict
YOLO11s on CPU, 768 px, NMS 0.7, confidence slider
3. Browser
Boxes, counts per class
and inference time
4. results/
annotated.jpg, detections.json, summary.csv, report.html
Also: model selector (.pt or .onnx), light and dark theme, recent-results panel, /health and /docs endpoints. Stack: FastAPI, Ultralytics, vanilla
HTML, CSS and JS.
Forklift and Pallet Detection · 14

## Slide 20
•Source: s0_forklift
•Image: rep1_s0_forklift__01FVZIGPUGWI_jpg.rf.272f9ea3336a11f2c4390ccc97244242.jpg •Detections: 1
•Class: forklift | Confidence: 0.907
VISUAL RESULTS
Predictions next to the labels
Forklift and Pallet Detection ·

## Slide 21
•Two datasets merged, filtered to two classes and audited •Train, validation and test splits without near-duplicate
•YOLO11n and YOLO11s trained and compared •Per-class evaluation and error analysis
1.Label real Petrochoice frames and review the pseudo-
labels
2.Improve data and model iteratively, with active learning 3.Validate on representative warehouse data
4.Optimize for the target hardware, then consider
deployment once targets are met
CONCLUSION
Done so far, and what comes next
Done
Next (proposed)
Forklift and Pallet Detection
•Deploy on FsstAPI and HTML CSS JS
Limitations
Public images may differ from Petrochoice cameras. Small and hidden pallets are the weak spot. Sources label one class each. The test set is small. Ultralytics is AGPL-3.0, check dataset licenses.

## Slide 22
PETROCHOICE · AI ENGINEER CANDIDATE · ROUND 2
Thank you.
Questions?
Rana Nasser